September 15, 2011
Standard 4inch Stage Controller 20C-200C:
The objective of these tests are to determine if a heater is needed with the standard 4-inch stage controller. Also, we would like to determine the appropriate power supply to use with this controller. The benefits of eliminating the heater are safer water temperatures and reduced hardware which eliminates costs.

For the first test, we are comparing the performance of the controller with a 600W 36V power supply with and without the heater. The high voltage has been set to 42V(the maximum allowed for this power supply) and the low voltage has been set to 30V. At lower tempertaures the stage has lower resistance which causes high current to pass through the stage. To eliminate the high current through the stage the high voltage will not switch in until the stage reaches at least 40C. The water start and end temperatures are 30C and 60C, respectively, in both cases.

The stage reaches 200C almost 3 times faster with the heater, but we are supplying a maximum of only 11A to the stage. In both cases, we are waiting for the water to reach about 60C, obviously this happens faster with a heater. A better approach would be apply more voltage/current, so we are not waiting for the water to heat up.
Heater Vs. No Heater
36V 600W Supply Vhigh = 42V, Imax = 11A @ 40C
Time (s)
Temp (C)

For the next test, we are comparing the time it takes to heat the stage to 200C at three different voltages. We are going to use a 600W 48V supply and the high voltages will be set to 41V, 44V and 46V. The low voltage will be set to 30V and the starting water temperature will be 30C for all three cases. Once again the high voltage will not be applied until the stage reaches at least 40C.

When the high voltage is set to 41V, 44V and 46V, the ending water temperatures are 38C, 45C and 60C, respectively. By raising the voltage, we are eliminating the need for high water temperatures.
Standard 20C-200C 4-inch Controller 600W Supply No Heater
40C Switching Voltage
Time (s)
Temp (C)
The stages reaches 200C almost 6 times faster when the voltage across the stage is raised 5V. This indicates that raising the voltage is more effective than using a heater. The problem is raising the voltage can raise the current to beyond the power supplies capabilities. The 48V 600W supply can only supply 13A. When the high voltage of 46V is applied to the stage at 40C, the stage draws 16A of current. We can either use a higher wattage power supply, which can be expensive, or switch in the high voltage at a higher temperature/higher resistance. We will now compare the max current to the stage when switching in the high voltage when the stage reaches 40C, 86C and 120C.

Standard 20C-200C 4 Inch Controller 48V 600W No Heater
Vhigh = 46V, Vlow = 30V
Time (s)
Temp (C)
When we switch in high voltage of 46V at 120C, the maximum current to the stage is 12A. This is below the current requirement for the 48V 600W power supply. The ending water temperature is 38C.This eliminates the need for a heater in the system. If we switch the in high voltage at higher stage temperatures, the current is reduced, and the need for higher wattage power supplies is eliminated.

Standard 20C-200C 4-Inch Controller 48V 600W Supply No Heater
Vhigh = 46V, Vlow = 30V, Switch Voltage @ 120C Imax = 12A @ 120C

Above are plots of the controller heating the stage from 20C to 200C and vice-versa from various water start temperatures. This is meant to indicate normal operation. The worst case heat time is about 320s when the water start temp is approximately 30C(room temperature). The cool time doesn't seem to be affected by the starting water temperature and is approximately 180s.

Standard 4-inch 20C-200C Controller Suggestions:
- 48V 600W supply
- No heater
- Vhigh = 46V
- Vlow = 30V
- Switch in high voltage at 120C
  - Imax = 12A @ 120C

4inch Stage Controller -40C-200C (with neslab):
The Objective of these tests are to determine if a 48V 600W or 48V 1000W power supply is needed for this controller. The advantage to the lower wattage power supply is it is significantly cheaper than the 1000W supply.

We will first test the cooling capabilities of both supplies. The water start temperature is 25C and the low voltage will be set to 30V for both supplies. The stage will start at 200C and the controller will cool the stage to -40C. The neslab will cool the water to -10C.

600W vs 1000W Cooling Performance
600W Vlow = 30V Imax = 12A @ -40C 1000W Vlow = 30V Imax = 12A @ -40C
Time (s)
Temp (C)

The cooling performances are identical for the 1000W and 600W supply. Next we will test the heating performance for both supplies. For the 600W supply, we will use the same setup as the standard 4-inch 20C-200C controller. We will switch in the high voltage of 46V when the stage reaches at least 120C. This setup worked very well for the for the standard 4-inch 20C-200C controller, but in this case we will be fighting lower water temperatures and may need extra power. The 1000W power supply can supply up to 23A, so we are able to apply more voltage to the stage. Also, we can switch in the high voltage at a lower stage temperature, because the 1000W supply has higher current capabilities. For the 1000W supply, we will switch in the high voltage of 48V when the stage reaches reaches 40C. The starting water temperature is -5C, which will be considered the worst case for heating. The neslab will heat the water to 25C. The graph comparing the the heating performance of the 1000W to the 600W supply is below.

600W vs 1000W Heating Performance
1000W Vh = 48V, Imax = 20A @ 40C 600W Vh = 46V Imax = 13A @ 120C
Time(s)
Temp (C)
The 1000W supply can heat the stage to 200C almost twice as fast as the 600W supply. The ending water temperatures for the 600W and 1000W supplies are 20C and 12.5C, respectively. This indicates that the 600W supply has to wait for the water to heat an additional 7.5C before the stage can reach 200C.

Advantages of the 1000W supply:
~2x faster heat time than 600W supply (in worst case)

Disadvantages of 1000W supply:
- 1000W supply is significantly more expensive than the 600W supply
- Higher current system (20A+)
  - The controller will require a high current connector
  - Require high current relays(40A crydoms)
- If the 600W supply is used, the standard 4-inch 20C-200C controller will be identical to the 4-inch -40C-200C controller.